Weekly Meeting 05/10
Hardware & Software Design Discussion
- Jingyan Ling

---
Hardware Design
- Equipment Goal:
  - 1. Make sure torso is straight
  - 2. Make two shoulders at same level
  - 3. Lock wrist joint
  - 4.	Adjust configuration of arms
    - Allow 2 dof on shoulder
    - Allow 1 dof on elbow (with surface constrain)

---
Configuration Variables
Corresponding Joint on Body	Configuration Description	Notation	Desired Value Range	Comment
Shoulder	Chest – Upper Arm	alpha	85
Shoulder	Torso – Upper Arm	beta	40
Elbow	Upper Arm - Forearm	gamma	90

---
Hardware Design
- Equipment Goal:
  - 5. Quick set up
  - 6. Quick Measurement

---
Hardware Design
- Equipment Goal:
  - 1. Make sure torso is straight
  - 2. Make two shoulders at same level
  - 3. Lock wrist joint
  - 4.	Adjust configuration of arms
    - Allow 2 dof on shoulder
    - Allow 1 dof on elbow (with surface constrain)
Interest Point * Attraction for kids

---
1.Make Torso Straight
  - Shoulder can be considered as sphere joint (3 dof).
  - Adding one constraint to lower dof
  - Approach:
    - Seat belt
    - Posture Brace

---
2. Fix shoulder level
- Small blocks that can slide on chair back
- Gently touch shoulder and provide constrain (Do not need to press hard)
- * Make it looks like little wings

---
4. Adjustable configuration variables
- Desk
  - Adjustable in height
  - Adjustable in the direction towards or away from subject
  - On desk:
    - Adjustable horizontal position for force sensors (elbow position)
    - Revolution Joints underneath force sensors
    - * Cartoon Painting on desk

---
Desk Design

---
6. Quick Measurement
- Approach:
  - 1. Manual Measurement
  - 2. Camera + AR tags
    - Two cameras on shoulder block
    - Two AR tags for each arm
      - One besides force sensor
      - One at tip of arm (finger position)
    - Read transformation matrix seen from camera to AR tags.

---
Software Design
- Pipeline
DAQ
Python
Pygame
DAQ
MATLAB
Simulink
ROS on Windows

---
Game Design
- Ski-like game
- Character rushes towards hill
- Speed depends on torque
- Change hill size for
  different torque to
  go through the hill